## Slide 1: Volume 5 Waste
2006 IPCC Guidelines
Bonn, 18 may 2006
Riitta Pipatti

## Slide 2: IPCC 2006 GLs: Waste Volume
Riitta Pipatti (Finland) and Sonia Viera (Brazil)
Joao Alves (Brazil), Michiel R. J. Doorn (Netherlands), Qingxian Gao (China), Sabin Guendehou (Benin), Leif Hockstad (USA), William Irving (USA), Matthias Koch (Germany), Carlos López (Cuba), Katarina Mareckova, (Slovakia), Hans Oonk (the Netherlands), Craig Palmer (Canada), Elizabeth Scheehle (USA), Sharma Chhemendra (India), Alison Smith (UK), Per Svardal (Norway), Sirintornthep Towprayoon (Thailand), Masato Yamada (Japan) and Can Wang (China)

## Slide 3: Contents of the presentation
Waste Volume - contents
Activity data collection (solid waste)
Waste categories
  Overview of methodological issues and challenges in reporting
Conclusions

## Slide 4: Waste Volume - contents
1 Introduction
2 Waste generation, composition and management data
3 Solid waste disposal
4 Biological treatment of solid waste
5 Incineration and Open Burning of Waste
6 Wastewater treatment and discharge

## Slide 5: Activity data for solid waste
Waste generation, composition and management data
  encourage collection and use of country-specific data (local conditions vary much; uncertainties for default data large)
  regional/country-specific default data on amounts, management and waste composition
  management data: solid waste disposal, incineration, composting and other (recycling)
  consistent treatment across categories

## Slide 6: Activity data for solid waste
Default waste categories: MSW, Sludge, Industrial waste and Other
  regional defaults for MSW components (paper, food, wood, plastics, etc.)
  defaults for carbon contents in the different waste types
    degradable organic carbon (SWDS)
    fossil carbon (incineration, open burning)

## Slide 7: Solid waste disposal
Significant source of methane
Considerable time lag in emissions after disposal - taken into account in the First order decay model (revised from GPG2000; spreadsheet; can be used for all Tiers)
  default parameters provided (updated values - decay rates by climate zone)
  default regional acitivity data (guidance how to estimate historical disposal)
  methane recovery - guidance improved

## Slide 8: Solid waste disposal
Provide data for HWP estimates
  FOD model produces estimates on carbon storage in SWDS
  only long-term carbon storage estimated
  also corresponding methane estimates
  carbon storage taken into account in the AFOLU/HWP section => long-term carbon storage reported as an information item in the Waste sector

## Slide 9: Solid waste disposal

## Slide 10: Biological treatment of solid waste
GHG (CH4, N2O) emissions from biological treatment small (CO2 not taken into account as of biogenic origin)
simple methdology - activity data times emission factor (defaults provided for composting and anaerobic digestion)
energy use of methane from anaerobic digestion => emissions from combustion to be reported in the Energy sector

## Slide 11: Incineration and open burning of waste
Waste-to-energy reported in the energy sector
CO2 from fossil waste fractions (plastics, waste oils, etc.), N2O and CH4
open burning - new category; important in developing countries

## Slide 12: Wastewater treatment and discharge
improved guidance (incl. tier-structure)
wastewater and sludge - emissions during treatment estimated together (organic matter in sludge disposed at SWDS, spread in agricultural soils or incinerated subtracted)
uncollected wastewater - methodology
N2O - methodology also for industrial waste water treatment

## Slide 13: Conclusions
Guidance complemented, revised (e.g. FOD model) and default activity data and parameters improved
a more systematic approach to waste management
Good quality activity data (amounts, waste compostion, BOD/COD in wastewater, management/treatment data) - data improving in many countries but still a challenge