## Slide 1: The Use of Tier 3 Systems to Factor Out Non-Anthropogenic Emissions and Removals on Managed Land
Dr Gary Richards
Department of Climate Change
Australia
Notes: <number>
This presentation looks at the use of Tier 3 methods to factor out non-anthropogenic emissions on managed lands. The use of models to factor out natural disturbances, indirect effects and climate variability is explored.

## Slide 2: Non-anthropogenic emissions
There are many direct and indirect sources and sinks of greenhouse gases on managed land, including:
  natural disturbances
  climate variability
  CO2 fertilisation and N-deposition
  forest age class legacy effects
Notes: There are many sources of non-anthropogenic emissions and these can be indirectly due to human activity (e.g. legacy effects) or entirely natural (e.g. wildfire). Each has different characteristics and requires different treatment to separate them from anthropogenic emissions.
<number>

## Slide 3: Human management
Human land management is not independent, but often is either causal or responsive to effects such as climate variability
  as management is not independent makes factoring out more difficult, and pragmatism more necessary
The separation of managed and unmanaged land is a good first step
Notes: Emissions can vary according to management, or with climate variations under the same management. Management and climate are often intertwined as management responds to climate.
<number>

## Slide 4: Can Tier 3 models help?
Yes, and Land Representation Approaches also have a role
  on lands where emissions are overwhelmingly natural, it may be appropriate to remove those lands (incl. sources and subsequent sinks) from accounting (e.g., for stand replacing forest fires)
As there are few anthropogenic emissions in these circumstances, models may not be needed
Notes: In some cases the emissions from natural disturbance may be so overwhelming of any anthropogenic emissions that it may be more effective to remove the land from accounts rather than try to separate out the non-anthropogenic emissions.
<number>

## Slide 5: How can models be used?
Models can be used to separate anthropogenic and natural emissions from:
  impacts of past management
  climate variability
  CO2 fertilisation and N-deposition
Not all models do all of these
Models must be supported by good calibration and validation data
Robust modelling requires extensive data inputs
Notes: Well calibrated models with appropriate input data can be used to separate out natural emissions that would otherwise be measured in by measurement approaches. Not all forms of models can be used for factoring out.
<number>

## Slide 6: Model forms
The two main genres of models are:
  Empirical: founded on long term observations – they range from simple summaries of data to complex additive (factors) models
  Process: place more emphasis on biophysical management and climate interactions
Simply, empirical models are based on observations, and process models are built for prediction
Notes: Models can be empirical in nature and at their simplest be statistical interpretations of long term measurements. They may represent different management systems, climate zones etc. Process models summarize biological function and are responsive to real-time climate drivers.
<number>

## Slide 7: Model calibration
Properly calibrated empirical and process models should yield the same results
  process models: can be used to determine plant and microbial response to climate variations and management
  empirical models: tend to average out variability by summarising long term data
Both model forms must be well ‘fitted’ (calibrated) and able to be applied elsewhere (validated)
Notes: Both forms of models need to be properly calibrated and validated for their ability to be portable to new situations.
<number>

## Slide 8: Models and management
Empirical models often embed a management system – if data is available then a variety of management systems can be represented
Process models may or may not reflect management systems, depending on how this is done management systems (or lack of) may be modelled
Notes: Empirical models will typically reflect a “class” of management whereas process models, if they reflect management, do so in a way responsive to climate conditions at that time.
<number>

## Slide 9: Models and legacy effects
Models (both empirical and process) that use age class (and possibly management system) can be used to separate out legacy effects from past management
Many process models predict ‘potential’ biomass and soil carbon accumulation – the prediction of potential instead of actual does not support separation
Notes: For models to be able to identify legacy effects, they must use information on past human activities leading to ongoing emissions and removals. Both empirical and process models can achieve this.
<number>

## Slide 10: Models and climate effects
As empirical models are founded on observations they typically ‘average out’ the effects of variability and trends in climate
Process models are sensitive to climate conditions for growth, turnover and decomposition rates, and can reflect, if calibrated to do so, extreme events
Notes: As climate is a key driver in process models, they can be used to test scenarios of climate variability and change. As climate affects many model components, e.g. growth, turnover and decomposition, it is important that ALL affected model components are treated in the same way. Dealing with just one component, say decomposition of litter or soil, will give corrupted results.
<number>

## Slide 11: Models and indirect effects
Empirical models factor in effects such as CO2 fertilisation and N-deposition through their measured inputs, i.e., data used to form the models include these effects.
Process models may or may not contain algorithms to reflect these effects:
  models are only as good as the data used to calibrate them, so if there is uncertainty in the science as to the extent and longevity of an effect, then the models can only reflect this uncertainty
Notes: Models can contain algorithms to deal with indirect effects, but the issue remains about the certainty of the effects and having sufficient data to calibrate and validate models.
<number>

## Slide 12: The Australian experience
Australia uses a hybrid of empirical and process modelling, i.e., a process model constrained by observational data
The models reflect age class, climate, management and bio-physical condition
The integrated modelling framework allows for testing of changes in management and legacy effects under different climate conditions.
Indirect effects (CO2 and N dep.) are not included as no conclusive data is available for model calibration
The spatially explicit (Approach 3) coupling can identify where natural disturbances occur, and the sources and sinks from those disturbances
Notes: Australia uses an integrated (all pools) hybrid process model, directly coupled with Approach 3 (remote sensing) data in a grid-based model. The model can deal with management changes, legacy effects, climate variability and separate identification of natural disturbances. There is as yet not sufficient data or certainty to impose routines for indirect effects.
<number>

## Slide 13: Variability and natural disturbance
The effects of natural disturbance and climate variability on Australia’s national accounts (all sectors) are shown above when comparing a managed land construct (equivalent to comprehensive Article 3.4 inclusion) to the activity based accounting of the 1996 Guidelines
Notes: The impact of the managed land construct without any subsequent treatment of variability of natural disturbance is extreme for Australia. The results show the modelled estimates of the managed lands approach compared to the 1996 Guidelines, on a complete all sectors national inventory.
<number>

## Slide 14: Conclusion
Some models can be used to separate out various forms of natural emissions, and some factor these in by default
Models that can comprehensively achieve this are very data-hungry for calibration and validation, and for ongoing operation
Measurements and most empirical models ‘measure in’ most sources of natural emissions (and typically smooth out variability) while process models can include or exclude variability
  reporting and accounting policy needs to consider these differences
Notes: Models can be of great utility in factoring out non-anthropogenic emissions on managed land. The appropriate form of model will depend on what is to be factored out. As currently different estimation approaches will give different representations of variability and some factor out and some factor in legacy and indirect effects, greater certainty in reporting policy is required. Reporting policy, not methodological choice, should guide these issues.
<number>