## Slide 1: Treatment of “Anthropogenic” Emissions/ Removals in IPCC GHG Inventory Guidelines
Nalin Srivastava
Expert Meeting on Revisiting the use of Managed Land as a Proxy for Anthropogenic Emissions and Removals
5 -7 May, 2009 INPE, São José dos Campos, Sao Paulo, Brazil
Notes: <number>

## Slide 2: Outline
Introduction
IPCC approach toward estimating terrestrial anthropogenic emissions and removals
Treatment of anthropogenic emissions and removals in the IPCC Guidelines
  The Revised 1996 IPCC Guidelines
  GPG-LULUCF
  2006 IPCC Guidelines
Conclusion
Notes: <number>

## Slide 3: Human impact on terrestrial GHG fluxes
Human intervention has been a significant driver of the change in global C cycle and consequently climate change
Terrestrial biosphere is a key determinant of the composition of the atmosphere
Human intervention influences a wide variety of ecosystem processes responsible for greenhouse gas fluxes
The UNFCCC asks for separation of anthropogenic from natural terrestrial GHG fluxes
Notes: <number>

## Slide 4: IPCC approach toward estimating terrestrial anthropogenic emissions and removals
Notes: <number>

## Slide 5: Main greenhouse gas emissions/removals processes in managed ecosystems
Methanogenesis
Photosynthesis
Methanogenesis
Nitrification & denitrification
Oxidation
Oxidation
Notes: <number>

## Slide 6: Special features of terrestrial GHG fluxes
Terrestrial GHG fluxes are characterized by a great degree of spatial heterogeneity and temporal variability
Difficult to identify and distinguish between natural and anthropogenic factors and establish causality in terms of human actions
‘Indirect’ human induced effects such as CO2 fertilization and N-deposition also significant
Notes: <number>

## Slide 7: The idea of managed land as a proxy for anthropogenic effects
Inventory methods have to be operational, practical and globally applicable while being scientifically sound
IPCC Guidelines have taken the approach of defining anthropogenic greenhouse gas emissions and removals by sinks as all those occurring on ‘managed land’
‘Managed land is land where human interventions and practices have been applied to perform production, ecological or social functions’
Managed land has to be nationally defined and classified transparently and consistently over time
GHG fluxes need not be reported for unmanaged land
Notes: <number>

## Slide 8: Basis for managed land as a proxy for anthropogenic effects
Notes: <number>

## Slide 9: Treatment of anthropogenic emissions and removals in the IPCC Guidelines
Notes: <number>

## Slide 10: IPCC Guidelines for National Greenhouse Gas Inventories
Revised 1996 IPCC Guidelines
2000 Good Practice Guidance and Uncertainty Management(GPG2000)
Good Practice Guidance for Land Use, Land-Use Change and Forestry (GPG-LULUCF)
2006 IPCC Guidelines for National Greenhouse Gas Inventories(2006 IPCC Guidelines)
Notes: <number>

## Slide 11: IPCC Guidelines
Provide the methodological basis for reporting of national GHG inventories by the Parties to the UNFCCC
1996 IPCC Guidelines along with GPG2000 and GPG-LULUCF are mandatory for Annex-I countries for reporting under UNFCCC and encouraged for other Parties
Notes: <number>

## Slide 12: Revised 1996 IPCC Guidelines
Contained guidance only on the main terrestrial activities and processes responsible for significant GHG fluxes
Divided terrestrial sources/sinks into two sectors, viz. Agriculture and Land Use Change and Forestry (LUCF)
Agriculture and LUCF consisted of 7 and 5 categories respectively
Notes: <number>

## Slide 13
4A. Enteric Fermentation
4B. Manure Management
4C. Rice Cultivation
4D. Agricultural Soils
4E. Burning of Savannas
4F. Field Burning of Agricultural Residues
4G. Other
5A. Changes in Forest & Other woody biomass stocks
5B. Forest and Grassland Conversion
5C. Abandonment of Managed lands
5D. CO2 Emissions and Removals from Soil
5E.Other
Agriculture
LUCF
Notes: <number>

## Slide 14: 1996 Guidelines: managed land proxy
As the 1996 IPCC Guidelines only include the processes occurring on lands subject to human intervention, they implicitly assume managed land as a proxy for anthropogenic emissions
  Changes in Forest and Other Woody Biomass category excludes natural unmanaged forests.
  Forests re-growing naturally on abandoned lands included in the category Abandonment of Managed lands only if carbon uptake attributable to past human activities
Notes: <number>

## Slide 15: 1996 Guidelines: indirect anthropogenic effects
Indirect anthropogenic effects not explicitly addressed, though estimation methods can capture indirect effects on managed land
Acknowledge but do not address the effect of indirect anthropogenic effects on unmanaged land due to a lack of scientific understanding
  1996 Guidelines state that natural un-managed forests may indeed be sinks and recommend that tropical countries need to establish permanent forest inventories to determine whether undisturbed forest are sinks or not
Notes: <number>

## Slide 16: 1996 Guidelines: fires and natural disturbances
Address burning in management of forests and woody biomass and conversion of forest and grasslands respectively as well as prescribed burning of savannas and agriculture residues
The effects of wildfires and natural disturbances on managed land not explicitly dealt with but can be considered implicit in Changes in Forest and Other Woody Biomass estimations
Notes: <number>

## Slide 17: 1996 Guidelines: natural emissions and removals on unmanaged lands
Include some discussion of the natural background emissions or removals (e.g. CH4, N2O, CO etc.) from unmanaged land but only in the context of their conversion to managed land
  But guidance left for the future
Notes: <number>

## Slide 18: 1996 Guidelines: inter-annual variability
Inter-annual variability of GHG fluxes has not been explicitly addressed
Notes: <number>

## Slide 19: GPG2000
Provided supplementary information to help develop good practice inventories that “…contain neither over nor under-estimates as far as can be judged, and in which uncertainties are reduced as far as practicable”
Contained guidance on only the Agriculture sector
Retained the structure and source/sink categories of the 1996 IPCC Guidelines
Notes: <number>

## Slide 20: GPG-LULUCF
Extended the good practice guidance to entire LULUCF sector and reorganized all emissions and removals from all land use activities into six broad land-use categories, namely:
  Forest Land
  Cropland
  Grassland
  Wetlands
  Settlements
  Other lands
Notes: <number>

## Slide 21: 2006 IPCC Guidelines
Integrated Agriculture and LUCF sectors in the 1996 IPCC Guidelines in to one sector called Agriculture Forestry and Other Land Use (AFOLU) to improve the general consistency and completeness of the national inventories
Retained the structure of six land use categories of GPG-LULUCF
Notes: <number>

## Slide 22: GPG-LULUCF & 2006 IPCC Guidelines: managed land proxy
GPG-LULUCF explicitly adopted the approach of using managed land as a proxy for anthropogenic emissions and removals for the first time
Reporting of emission and removals confined to managed lands
Emissions and removals on unmanaged land not to be reported …
Retained and made more explicit by 2006 Guidelines
Notes: <number>

## Slide 23: GPG-LULUCF & 2006 Guidelines: indirect anthropogenic emissions
Both in GPG-LULUCF & 2006 IPCC Guidelines, estimation methods capture the indirect anthropogenic effects such as CO2 fertilization and N-deposition on managed lands only
Indirect anthropogenic effects on unmanaged lands not included in the reporting framework
Notes: <number>

## Slide 24: GPG-LULUCF & 2006 Guidelines: fires and natural disturbances
In both GPG-LULUCF and 2006 Guidelines, GHG effects from all natural disturbances (wild fires, insect, storms etc.) to be reported only on managed lands
GHG effects from all natural disturbances to be reported for unmanaged lands only if followed by land use change to managed land
Effects of both wildfires and prescribed burning on managed lands should be included (CO2 & non-CO2 for Forestland and only non-CO2 for Grassland etc.)
Notes: <number>

## Slide 25: GPG-LULUCF & 2006 Guidelines: fires and natural disturbances(2)
In GPG-LULUCF, CO2 emissions from wildfires and prescribed burnings on managed forests need not be reported if the removals due to subsequent re-growth not captured in the estimation methods
In 2006 Guidelines, CO2 fluxes from wildfires and prescribed burnings have to be mandatorily reported together with the subsequent re-growth
This approach in 2006 Guidelines addresses the issue of non-equivalence of re-growth due to non-maintenance of soil fertility etc. and captures the actual annual emissions more accurately
Notes: <number>

## Slide 26: GPG-LULUCF & 2006 Guidelines: natural emissions and removals on unmanaged lands
Both mention increase/decrease of background fluxes of non-CO2 gases (CH4 &N2O) from unmanaged lands such as undisturbed forest and wetlands but only in the context of conversion to managed lands
Guidance on these fluxes absent due to lack of scientific information
Notes: <number>

## Slide 27: GPG-LULUCF & 2006 Guidelines: inter-annual variability
Both GPG-LULUCF and 2006 Guidelines aim to estimate the actual annual emissions including inter-annual variability.
  They note that use of gain-loss method will some smooth out some annual variability.
  However, impacts of actual disturbances should be included.
  Tier 3 models should better estimate annual variability due to disturbances through model parameterization and validation using empirical research
Notes: <number>

## Slide 28: Conclusions
IPCC Guidelines have provided detailed methods to help countries report their terrestrial emissions and removals to the UNFCCC
The attribution of terrestrial GHG fluxes to anthropogenic causes is required for UNFCCC reporting
IPCC methodology have always either implicitly or explicitly used ‘managed’ land as a proxy for anthropogenic emissions
The IPCC Guidelines describe the use of this proxy in a consistent but progressively more refined approach
Notes: <number>

## Slide 29
Thank You!
IPCC Guidelines in all six UN languages can be downloaded from www.ipcc-nggip.iges.or.jp
Notes: <number>