## Slide 1: Uncertainty Analysis in Emission Inventories
Africa Regional Workshop on the Building of Sustainable National
Greenhouse Gas Inventory Management Systems, and the use of the 2006
IPCC Guidelines for National Greenhouse Gas Inventories
Swakopmund, Namibia
24-28 April 2017
Baasansuren Jamsranjav, IPCC TFI TSU

## Slide 2: Introduction
Uncertainty estimates are an essential element of a complete inventory of GHG emissions/removals
Uncertainty: a lack of knowledge of the true value of a variable that can be described as a probability density function (PDF) which describes the range and relative likelihood of possible values
Quantitative uncertainty analysis is performed by estimating the 95 percent confidence interval of the emissions and removals estimates for individual categories and for the total inventory
  95 percent confidence interval is enclosed by the 2.5th and 97.5th percentiles of the PDF

## Slide 3: Probability Density Function

## Slide 4: Probability Density Function

## Slide 5: Specifying Uncertainty
Uncertainty is quoted as the 2.5th and 97.5th percentiles i.e. bounds around a 95 percent confidence interval
This can be expressed, for example:
  234 ± 30%
  26400 (- 50%, + 100%)

## Slide 6: Benefits of Uncertainty Analysis

## Slide 7: Uncertainty Estimation
Gather Information
Collect uncertainty information on activity data and emission factors
Decide approach to use
Error Propagation
Monte Carlo
Perform Inventory Analysis
Spreadsheet
Software tool

## Slide 8: Sources of Uncertainty
Assumptions and methods
  The method may not accurately reflect the emissions
Input Data
  Measured values have errors and EFs may not be truly representative
  Lack of data (e.g. use of proxies, extrapolation)
Calculation errors
  Good QA/QC to prevent these

## Slide 9: Sources of Data and Information
There are three broad sources of data and information
  Information contained in models. Models can be as simple as arithmetic multiplication of AD and EF for each category and subsequent summation over all categories, but they may also include complex process models specific to particular categories
  Empirical data associated with measurements of emissions, and activity data from surveys and censuses
  Quantified estimates of uncertainties based upon expert judgement
Data collection activities should consider data uncertainties. This will ensure the best data is collected and ensures good practice estimates
Wherever possible, expert judgement should be elicited using an appropriate protocol (e.g. Stanford/SRI protocol)

## Slide 10: Methods to Combine Uncertainties
Approach 1: Error Propagation
  Simple (standard spreadsheet can be used)
    Guidelines provide equations and explanations
  Difficult to deal with correlations
  Standard deviation/mean < 0.3
Approach 2: Monte Carlo Method
  More complex (specialised software is used)
    Select random values of input parameters from their pdf and calculate the corresponding emission. Repeat many times and the distribution of the results is the PDF of the result from which mean and uncertainty can be estimated
  Needs information on PDF (mean, width, shape)
  Suitable where uncertainties large, non-normal distribution, complex algorithms, correlations exist and uncertainties vary with time

## Slide 11: Error Propagation
Enter Emissions Data
Enter Uncertainties
Data Calculated using simple equations

## Slide 12
Note short list of source/sinks
EF uncertainties based on defaults in guidelines
AD uncertainties based on source of data

## Slide 13: Illustration of Monte-Carlo Method

## Slide 14: Example of Monte Carlo Results

## Slide 15: Summary Results

## Slide 16: IPCC Inventory Software: Uncertainty Analysis
Click “Uncertainty Analysis”
Click to perform analysis

## Slide 17: IPCC Inventory Software: Uncertainty Analysis (cont.)
Click to enter AD and EF uncertainties

## Slide 18: Summary
Even simple uncertainty estimates give useful information - If they are performed well
Assessment of uncertainty in the input parameters should be part of the data collection
  Careful consideration will improve estimates as well as providing input data for uncertainty analysis
If resources limited: effort spent on uncertainty analysis should be small compared with total effort
At its simplest a well planned uncertainty assessment should only take a few extra hours!
  Uncertainty in AD assessed as data collected
  Uncertainty in EFs from guidelines now available
  Aggregate categories/gases to independent groups of sources/sinks
  Use Approach 1

## Slide 19
Thank you